## Slide 1
AI Hardware Project
Edge-AI Waste Classification on OpenMV H7
Course: AI Hardware
Members: Mengzi Cheng, Shuai Tu, Sirui You, Xueyi Zhang
Team Name : Circuit Board Layout
Date: December 2025

## Slide 2
01
02
03
04
05
06
Platforms ＆ Team Responsibilities
CONTENTS
Conclusions ＆ Future Works
Dataset & Preprocessing
Motivation＆ Goals
Model & Training
Deployment & Results

## Slide 3
Platforms ＆ Team Responsibilities
01

## Slide 4
Platforms
1
Category | Key Spec | Value
Compute | MCU | STM32H743II, ARM Cortex-M7
Compute | Clock | 480 MHz
Memory / Storage | RAM / Flash (total) | 33 MB RAM / 34 MB Flash
Camera | Sensor | OV5640 (5MP, up to 2592×1944)
Camera | Lens | 2.8 mm, F2.0 (M12 mount)
Deployment | Model runtime | TensorFlow Lite (TFLite) support / OpenMV export workflow
Power | Input | VIN 3.6–5 V (3.3V logic)
Power | Current draw (active) | ~230–240 mA @ 3.3 V (with/without μSD)
I/O | Connectivity | USB FS (12 Mbps) + microSD slot
Form factor | Size / Weight | 45×36×29 mm / 17 g
Hardware Platform:
• OpenMV H7 (STM32H7 Cortex-M7 @ 480 MHz, camera module, various sensors, and support for TensorFlow Lite for Microcontrollers.)
Software:
• Edge Impulse
• OpenMV IDE

## Slide 5
Pipeline ＆ Team Responsibilities
1
Dataset
TrashNet
4 types: paper / plastic / metal / glass
Split & Upload
Train/Val split
Upload to
Edge Impulse
Preprocess
Resize + grayscale
96×96 input
Training
MobileNetV2
Transfer Learning
Export & Deploy
OpenMV export
TFLite + labels
Live Inference
Camera → probs
+ FPS output
Name | Role | Responsibilities
Mengzi Cheng | Team Leader | Planning & coordination; integration oversight; presentation coordination
Shuai Tu | Hardware & Deployment | OpenMV H7 setup; device/camera configuration; on-device deployment; demo hardware support
Sirui You | Software & Integration | OpenMV scripting; inference pipeline implementation; debugging & serial/logging integration
Xueyi Zhang | Model & Documentation | Proposal writing; PPT design/editing; dataset preparation; model training & evaluation; final report submission
Week | Milestone | Deliverable
2 | Proposal | PDF + GitHub submission
4 | Midterm presentation | model quantization and benchmarking, presentation slides
6 | Integration & testing | on-device inference, FPS/latency results, robustness testing and analysis
Dec.18 | Final presentation | Final report, demo video, slides, GitHub archive
Project Pipeline

## Slide 6
Motivation ＆ Goals
02

## Slide 7
Motivation
2
Why Edge AI for Waste Sorting?
Waste Classification
Fast & reliable sorting needs real-time decisions near the bin.
Cloud inference adds latency, needs connectivity, and raises privacy concerns.
Edge inference on MCU enables low-cost, low-power, standalone deployment.

## Slide 8
Project Goals & Success Metrics
2
GOAL
Build an end-to-end edge AI pipeline (dataset → training → deployment).
Deploy a waste classifier on OpenMV H7 for live camera inference.
Run fully on-device without cloud for standalone operation.
Evaluate performance under MCU constraints (accuracy, speed, memory).
Accuracy
Validation accuracy + confusion matrix
Latency/FPS
Real-time speed measured on OpenMV H7
Memory ＆ Footprint
RAM & Flash usage fits MCU limits
Robustness
Works across lighting/background with real objects
Deliverables
Model , OpenMV script , Demo video , Report, Presentation

## Slide 9
Dataset & Preprocessing
03

## Slide 10
Waste Image Dataset – Trash Net
3
Example images from the Trash Net
Plastic / Paper
Metal / Glass
Source: GitHub repository
Task: Single-image multi-class classification of household waste
Classes (4): glass, metal, paper, plastic
Image resolution: 512 × 384 pixels (RGB)
Acquisition setup: Captured with iPhone cameras under room light
Total number of images: 1,984

## Slide 11
Data Preprocessing
3
Offline preprocessing
Online preprocessing
Resize mode: keep the original aspect ratio
Convert each 96 × 96 grayscale image into a normalized feature vector
4 ms processing time and 4 KB peak RAM usage
All images are RGB
Resize to 512 × 384 pixels
Store in class-specific folders (glass, metal, paper, plastic)

## Slide 12
Model & Training
04

## Slide 13
Edge Impulse Platform for Embedded ML
4
In this project, we use Edge Impulse mainly for image classification of waste.
Module | Function | Our work in this project
Data acquisition | Import and organize datasets | Upload images from Trash Net and create labels in Edge Impulse
Impulse design | Define input, preprocessing, classifier | Set image size, normalization and image classification block
Model training | Train and optimize models | Run multiple trainings and tune epochs / batch size / augmentation
Model testing | Evaluate model performance | Check accuracy, loss curves and confusion matrix
Deployment (analysis) | Prepare export for edge devices | Check memory and latency estimates for OpenMV H7 target
Use the built-in “Transfer Learning (Images)” block as the image classifier.
The model takes the image features as input and outputs 4 classes: glass, metal, paper and plastic.

## Slide 14
Model configuration & training results
4
Model & training settings
Backbone: MobileNetV2 96×96 0.35 (0.1 dropout)
Output: 4 classes (glass, metal, paper, plastic).
Training cycles: 45;
batch size: 32
learning rate: 0.0005.
Validation set: 20% of the data, data augmentation enabled.
Validation performance
Accuracy: 72.1%, loss: 0.66
AUC: 0.92
weighted Precision / Recall / F1: ≈ 0.72
Paper is easiest to classify (≈89.7% recall), glass and plastic remain harder.
On-device performance
Inference time: 36 ms (per image).
Peak RAM usage: ≈ 215 KB
flash usage: ≈ 536 KB.
Feasible for real-time deployment on OpenMV H7.

## Slide 15
Deployment
＆ Results
05

## Slide 16
Model Deployment to OpenMV H7
5
Exported as OpenMV Firmware (.tflite + labels.txt)
Ensured model size fits the H7 Flash & RAM
Downloaded via “Deployment → OpenMV” in Edge Impulse
Relevant screenshots
1. Exporting the Model from Edge Impulse
2. Copying the model into the board
2. Performance snapshots (Head & Tail)
3. Running the inference script
Connected OpenMV through USB
Copied trained.tflite and labels.txt to OpenMV’s file system
Verified file names match the Python script
Initialized camera (RGB565, QVGA, 240×240 crop)
Loaded TFLite model using ml.Model()
Ran continuous prediction loopPrinted class probabilities and FPS through serial monitor

## Slide 17
On-device Real-time Inference Pipeline
5
Block 1 — Setup: camera + model loading
Initialize the camera stream (format/size/crop), then load the TFLite model (trained.tflite) and the class list (labels.txt). This prepares the device for real-time inference.
Block 2 — Per-frame inference and raw output
For each frame, the code runs net.predict([img]) to get per-class probabilities, prints them, and reports FPS. This is the “raw” frame-level classification signal.
Block 3 — Sliding-window majority vote (stabilization)
The best label from each frame is pushed into a fixed-length window (VOTE_WINDOW). The final output label is the most frequent label in the window, which reduces jitter from noisy single-frame predictions.
Block 4 — Final display and reporting
Compute the average confidence for the voted label within the window, overlay “label + avg_score” on the live image, and print the voted result to the console for debugging/demo.

## Slide 18
5
Results – Paper
Case 1 – Paper Tissue (Correct Classification)
Final label: Paper (majority vote)
Confidence: avg_score ≈ 0.99 (example from demo)
Speed: ~3.17 FPS (device-side, live stream)
Paper tissue is recognized accurately and efficiently in real time, with stable predictions enabled by majority voting.

## Slide 19
5
Results – Plastic
Case 2 – Plastic lid (Correct Classification)
Final label: Plastic (majority vote)
Confidence: avg_score ≈ 0.99 (example from demo)
Speed: ~3.17 FPS (device-side, live stream)
Paper tissue is also recognized accurately and efficiently in real time, with stable predictions enabled by majority voting.

## Slide 20
5
Results – Metal
Case 3 – Aluminum foil ball (Correct Classification)
Final label: Metal (majority vote)
Confidence: avg_score ≈ 0.97 (example from demo)
Speed: ~3.17 FPS (device-side, live stream)
Metal is a relatively more challenging category to recognize due to reflections and appearance changes, but the system still achieves correct real-time identification, with stable predictions enabled by majority voting.

## Slide 21
5
Results – Glass
Case 4 – Glass Cup (Correct Classification)
Final label: Glass (majority vote)
Confidence: avg_score ≈ 0.91 (example from demo)
Speed: ~3.17 FPS (device-side, live stream)
Glass is a challenging category to recognize because it is transparent and highly sensitive to lighting and reflections, but the system still achieves correct real-time identification, with stable predictions enabled by majority voting.

## Slide 22
5
Results Summary
Paper & Plastic:
Most stable and accurate in our demos—high confidence and quick convergence with majority vote.
Metal:
More variable due to reflections and viewpoint changes, leading to less consistent probabilities.
Glass:
Hardest category—transparency and background/lighting dependence make predictions fluctuate.
Overall:
The observed performance gap is paper/plastic (easier) vs. metal/glass (harder) under real on-device conditions.

## Slide 23
Conclusions ＆Limitations
06

## Slide 24
6
Conclusions
What we built
What we achieved
We demonstrate feasible real-time waste classification on a low-cost MCU platform under tight compute/memory constraints.
End-to-end edge AI waste classifier: dataset → training → deployment → live inference
On-device pipeline on OpenMV H7 (camera capture + preprocessing + TFLite inference)
Stabilized real-time predictions using sliding-window majority vote
Validation accuracy: ~72.1% on TrashNet (4 classes)
On-device speed: ~3.17 FPS (live stream on OpenMV H7)
Footprint fits MCU constraints: ~215 KB peak RAM, ~536 KB flash

## Slide 25
6
Limitations + Future Work
OUTPUTS
Next, we will focus on improving reliability through better data coverage and MCU-aware tuning.
Limitations
Domain shift: TrashNet images differ from real on-device scenes (lighting/background), reducing robustness.
Hard classes: Metal & glass are sensitive to reflections/transparency → higher confusion vs. paper/plastic.
Real-time constraint: End-to-end speed is ~3.17 FPS, limited by capture + preprocessing + inference + display/printing.
Future Work
Data (reduce environment impact)：Collect in-domain images under target conditions (multiple lighting/backgrounds, real objects).
Model (improve metal/glass)：Tune augmentation for reflections/low-light (brightness/contrast, blur, background clutter).
System (improve FPS & UX)：Measure latency breakdown and optimize bottlenecks (reduce printing/overlay cost, streamlined preprocessing).

## Slide 26
Thanks for listening
Course: AI Hardware
Members: Mengzi Cheng, Shuai Tu, Sirui You, Xueyi Zhang
Team Name : Circuit Board Layout
Date: December 2025